MEYLE-HD ball joints – designed to make Renault vans tougher

- Technically enhanced spares engineered to withstand the highest levels of strain help prevent repeat repairs

- MEYLE workshop advice: The ball joint on a Renault Master must not be replaced more than once

Hamburg, 09 February 2016. One of the most frequent causes of unscheduled workshop visits for many Renault van models are defective ball joints. With the MEYLE-HD ball joints, workshops now have a solution to reliably remedy joint failure on Renault Master and Trafic models. To achieve this, engineers at Wulf Gaertner Autoparts AG have reinforced the ball joint's individual components along with the corresponding tie rod end and control arm assemblies, all of which are supplied in superior MEYLE-HD quality.

Renault van models notoriously require frequent repair caused by premature ball joint failure. Insufficiently designed, the original part often fails under the continually heavy axle loads which typically occur in this type of vehicle.

This is why MEYLE-HD ball joints – developed by Hamburg manufacturer Wulf Gaertner Autoparts – are engineered to provide improved load-carrying capabilities. MEYLE-HD ball joints feature an extremely wear-resistant plastic socket. Specially formulated high-performance grease ensures full compatibility with the materials making up the joint, i.e. steel and plastics. Under all operating conditions, the grease provides a constant lubricant film between the ball pin and plastic socket thereby ensuring smooth movement in the ball joint. Owing to the technical improvements over the OE design, the MEYLE-HD ball joint for Renault vans, comes with an extended four-year guarantee, as do all items of the MEYLE-HD range.

MEYLE workshop advice I: The ball joint on a Renault Master II (MEYLE no.: 616 010 0005/HD) must not be extracted from the control arm more than once. A small groove on the ball joint indicates if the part has already been removed before. If there is a groove, the entire control arm assembly needs to be replaced. Extracting the ball joint a second time may result in a loss of press-out force, consequently leading to the ball joint not fitting tightly enough in the control arm. Following the replacement of either the ball joint or the entire control arm assembly, an axle alignment must be performed.

MEYLE workshop advice II: To enable workshops to offer comprehensive repair services to professional standards the company supplies MEYLE-HD ball joints (MEYLE ref.:16-16 010 0005/HD) and the corresponding MEYLE-HD quality tie rod end and control arm assemblies for the Renault Trafic III:

- MEYLE-HD tie rod ends (MEYLE no.: 16-16 020 0008/HD and 16-16 020 0009/HD)

- MEYLE-HD control arms (MEYLE no.: 16-16 050 0017/HD and 16-16 050 0018/HD)

Download our press releases and press pictures from www.meyle.com or order in electronic file format.

Contact:

- Public Relations von Hoyningen-Huene, Marc von Bandemer, phone: +49 40 416208-17, e-mail: mvb@prvhh.de

- Wulf Gaertner Autoparts AG, Annika Fuchs, phone: +49 40 67506-519, E-Mail: annika.fuchs@meyle.com

About the Company

Wulf Gaertner Autoparts AG develops, produces and sells top-quality and quality-certified spare parts for cars, vans and trucks for the independent aftermarket under the brands of MEYLE and MEYLE-HD. The Hamburg manufacturer’s portfolio currently includes more than 18,500 articles, covering practically every requirement on the market. Engineers at the company also focus on products and services which can improve processes within the workshop. The MEYLE engineers have developed around 750 parts for thousands of different vehicle models and have technically optimised such parts compared to those made by the original equipment manufacturers. These MEYLE-HD products are extremely resilient and have a long service life. There is a four-year guarantee on the unique feature of technically improved MEYLE-HD parts.

Wulf Gaertner Autoparts AG was founded in 1958 and is headquartered in Hamburg, Germany. The company operates in 120 countries. In addition to its state-of-the-art logistics centre in Hamburg, the company also operates subsidiaries and production sites worldwide.